## Slide 1: Nucleo Acquisition S/W Structure
Main Thread
Initialization
Sensor Bus Protcol #X
Initialization
Sensor Manager Class
Mutex
Sensor ManagerThread
Initialization
Timer -> create an array of CAN Messages to reflect the current Sensor States
Sleep Till Timer Event
CAN Message Queue Class
Mutex
CAN Message Fifo
CANager Thread
Initialization
Timer -> send CAN the next CAN message once the CAN bus is available
Sleep Till Timer Event
Sensor Data Output on CAN BUS
Sys Timer
External Sensor N
ID
Sample Period
Last Sample Sys Time
Internal Sensor N
ID
Sample Period
Last Sample Sys Time
DATA
DATA
ID
Data
ID
Data
ID
Data
ID
Data
CAN CONTROLLER (WIP)
CAN Receive Message
(i.e. Time Sync, etc.)
Input Control
Output Control

## Slide 2: Open House In-Car Structure
Daughter Board
Daughter Board
CAN
RPi Hat
GPS Serial Data
BPS Serial Data
9DOF I2C Data
Luminosity I2C Data
STM Nucleo
STM Nucleo
Raspberry Pi 3
Send UDP over Ethernet